## Slide 1: .NET of Things

## Slide 2: This is:
Electronics
Native C/C++
Anything Internet related
This isn’t:
100 Level Overview
.NET

## Slide 3: Word Cloud
C#
.NET Core
.NET Standard
UWP
Micro Controller Unit (MCU)
Gadgeteer
.NET MicroFramework
TinyCLR OS
Meadow

## Slide 4: Misc Tools You’ll Need
SD Card Formatter
Disk Imager
  Win32 Disk Imager
Windows 10 IoT Core Dashboard
Plus your normal .NET Coding Tools

## Slide 5: Demo App
Based on outside light
  Turn spaceship lights on or off
Constantly polling light sensor
  Polling over I²C protocol

## Slide 6: I²C Protocol
Eye Squared See
Synchronous Protocol
Requires Hardware Support
Message Process
  Writing Data
    Write Out Register
    Write Out Each Byte
  Reading Data
    Write Out Register
    Read Each Byte

## Slide 7: SparkFun Ambient Light Sensor
APDS-9301
https://www.sparkfun.com/products/14350

## Slide 8: Raspberry Pi
“Low Resources”
  1.4 GHz 64 bit ARM CPU
  1 GB RAM
  Pi 3 B+
Exposed Pins
  The Money Maker

## Slide 9: Three Options with .NET
Windows 10 IoT
Mono on Raspberry Pi
.NET Core on Raspberry Pi

## Slide 10: .NET Standard 2.0+ Benefits

## Slide 11: Windows 10 IoT
Version of Windows for non-general purpose devices

## Slide 12: Good
Required OS updates every few years
Enterprise Programming Model
  Service vs. Client vs. Full App
  Headed vs. Headless
Hardware Specific
  Doesn’t run on MCUs
No quick start to creating a new App
  Copy/Paste existing examples
Ugly
Amazing tooling
Top Tier Debugging
  Line-by-Line
  Remote over network
Familiar to Windows Devs
  Remote PowerShell, Command Line

## Slide 13: Headed vs. Headless
Headed:
  Has a UI
  Single app starts on device startup
Headless:
  No UI
  UI Stack is disabled
    Black screen when monitor attached

## Slide 14: IoT Dashboard
Handles downloading Windows Versions
Puts Windows IoT onto SD Cards
Remotely connects to IoT Devices
  Run commands

## Slide 15: Windows 10 IoT - Getting Setup
Download/Install IoT Core Dashboard
  https://docs.microsoft.com/en-us/windows/iot-core/downloads
Create New Project in VS
  Blank App (Universal Windows)
  Manually make some changes
Debug Remotely
  VS can find the target device

## Slide 16: Demo

## Slide 17: .NET on Raspberry Pi
Running on Linux
Mono vs .NET Core (Pre/Post 3.0)

## Slide 18: Good
Doesn’t get as much love as Core
Ugly
Access to all Linux tools you’re used to
Mono tools not in .NET Core
  Compile on-board
  AOT Compiling
.NET Standard
On-board debugging
Installed with apt-get
Mono

## Slide 19: Good
Remote Debugging is Slow
Can’t compile on ARM chips
Ugly
Remote Debugging Exists
Access to all Linux tools you’re used to
GPIO Support for Raspberry Pi in .NET Core 3.0
Installed with apt-get, or downloading
  With Snap for 3.0
.NET Core

## Slide 20: Pin Access
File API
  Linux loves File APIs
  Not available for all pins like I2C
P/Invoke
  For performance
  Requires low-level code

## Slide 21: Setting Up I2C Raspberry Pi
Not on by default
Run `<>` to run through setup
https://learn.sparkfun.com/tutorials/raspberry-pi-spi-and-i2c-tutorial/all

## Slide 22: WiringPi
Open Source library for working with pins on Raspberry Pi
Can compile yourself
  Do it on Raspberry Pi
http://wiringpi.com/download-and-install/

## Slide 23: Compiling Apps
.NET Core
  Specify `linux-arm` architecture
  Self Contained if you desire
  Can’t be done on ARM device
  `dotnet publish ./RaspbianNetCoreDemo -c Release -r linux-arm --self-contained`
    ~\bin\Release\netcoreapp3.0\linux-arm\publish
  `dotnet RaspbianNetCoreDemo .dll`
Mono
  Can be done on ARM device
  Compile with MonoDevelop on Linux
  `mono RaspbianNetCoreDemo.exe`

## Slide 24: New in .NET Core 3.0
ARM 64 support for Linux
  Not Windows Yet
Pin Bindings for Raspberry Pi
  Open Source at github.com/dotnet/iot
Installed with Snap
  An app package manager
  sudo apt install snapd
  sudo snap install dotnet-sdk --beta --classic

## Slide 25: Demo

## Slide 26: History Lesson - .NET MicroFramework
Legacy
Designed for MCUs
  RAM ~300KB
  CPU like Cortex-M3 @ 120 MHz
Limited in features
  No generics
Limited MCU selection
Open Source
  http://netmf.github.io/
Netduino 2 courtesy of https://www.wildernesslabs.co/

## Slide 27: Cons
Limited Language Feature Support
  No Generics
Required VS Extension to begin
  Only worked on Community Version of VS
  Maxed out at VS 2015

## Slide 28: Gadgeteer
Extension of .NET MicroFramework
Easy Prototyping Platform
  Expensive
Open Source
  https://archive.codeplex.com/?p=gadgeteer
GHIElectronics FEZ Hydra
with Button module

## Slide 29: TinyCLR OS
Created by GHI Electronics
  https://www.ghielectronics.com/tinyclr/features
Can be ported to custom hardware
Modules hosted on NuGet
Not open source
  Though documentation is
Supports native C/C++ code
No Generics Support

## Slide 30: FEZ Board
Fast and Easy
Arduino Pin Compatible
$10 – Lowest Price
ARM Cortex-M4
512 KByte flash
96 KByte SRAM

## Slide 31: Other GHI Boards/Offerings
Universal Compute Modules
  Meant for Prototyping or low volume devices
  Switch out module while working
SurfaceMount Compute Modules
  Modules solder to board
  84MHz to 400 MHz chips
UCM
G120 SCM

## Slide 32: TinyCLR OS – Getting Setup
Follow simple instructions online
  https://docs.ghielectronics.com/software/tinyclr/getting-started.html
Install “TinyCLR OS Project System” Extension to VS
  https://marketplace.visualstudio.com/items?itemName=ghielectronics.tinyclr-projectsystem
Create new project

## Slide 33: TinyCLR Config
Application to update device Firmware
Debug board
Might need this on first use of new board

## Slide 34: Good
No Generics Support
Can’t reference .NET Standard Libraries
Use Threads, not Tasks
Closed Source
Ugly
NuGet Packages
Line-by-Line Debugging
Copies Win10 IoT API

## Slide 35: Demo

## Slide 36: Meadow Board
Created by Wilderness Labs
.NET 2.0
  Runs on top of Mono Runtime
No Board -> No Demo
Documentation: beta-developer.wildernesslabs.co
Very Early Days

## Slide 38: Getting Setup - Dev Machine - Windows
Follow Instructions per OS
  Windows, Linux, and MacOS
VirtualBox to run Vagrant
Vagrant
  VM software for development machines
  Download custom Vagrant file and config.sh from Wilderness Labs
dfu-uti*
  Used to send Meadow OS and/or Your App to Meadow board
  * This util comes with Vagrant setup. Download to your OS if you want to
Downloads Link
  http://beta-developer.wildernesslabs.co/guides/Getting_Started/Downloads/index.html

## Slide 39: Getting Board Setup
Purchase ST-Link V2
  For connecting Meadow board to host computer over USB
Download ST-Link software
Download dfu-util
  Device Firmware Upgrade Utilities
Flash Meadow Board with dfu-util

## Slide 40: Writing a Meadow App in VS
Create new Console App
  .NET Framework 4.7.1
  Same on MacOS, just extra steps
Add the Meadow.Core NuGet package
Change assembly name to app
  Meadow OS is hard coded to only run ‘app.exe’
  Not sure if this is temporary
Create any Class Libraries as .NET Framework
  Not Standard

## Slide 45: Extras
Hastlayer
  C# on FPGA
  Open Source
  https://hastlayer.com