## Slide 1: .NET of Things

## Slide 2: This is:
Electronics
Native C/C++
Anything Internet related
This isn’t:
100 Level Overview
.NET

## Slide 3: Word Cloud
C#
.NET Core
.NET Standard
UWP
Gadgeteer
.NET MicroFramework
TinyCLR OS
Meadow

## Slide 4: Demo App
Based on outside light
  Turn spaceship lights on or off
Constantly polling light sensor
  Polling over I²C protocol

## Slide 5: I²C Protocol
Eye Squared See
Synchronous Protocol
Requires Hardware Support
Message Process
  Writing Data
    Write Out Register
    Write Out Each Byte
  Reading Data
    Write Out Register
    Read Each Byte

## Slide 6: SparkFun Ambient Light Sensor
APDS-9301
https://www.sparkfun.com/products/14350

## Slide 7: Raspberry Pi
“Low Resources”
  1.4 GHz 64 bit ARM CPU
  1 GB RAM
  Pi 3 B+
Exposed Pins
  The Money Maker

## Slide 8: Three Options
Windows 10 IoT
Mono on Raspberry Pi
.NET Core on Raspberry Pi

## Slide 9: Windows 10 IoT

## Slide 10: Pros
No Generics Support
Cons
Amazing tooling
Top Tier Debugging
  Line-by-Line
  Remote over USB (or network???)
Required updates every few years
Meh?

## Slide 12: .NET Core on Raspbeery Pi

## Slide 13: Pros
Still preview after a few years
Cons
Amazing tooling
Top Tier Debugging
  Line-by-Line
  Remote over USB (or network???)
Required updates every few years
Meh?

## Slide 15: .NET MicroFramework
Legacy
Designed for MCUs
  RAM ~300KB
  CPU like Cortex-M3 @ 120 MHz
Limited in features
  No generics
Limited MCU selection
Open Source
  http://netmf.github.io/
Netduino 2 courtesy of https://www.wildernesslabs.co/

## Slide 16: Cons
Limited Language Feature Support
  No Generics
Required VS Extension to begin
  Only worked on Community Version of VS
  Maxed out at VS 2015

## Slide 17: Gadgeteer
Extension of .NET MicroFramework
Easy Prototyping Platform
  Expensive
Open Source
  https://archive.codeplex.com/?p=gadgeteer
GHIElectronics FEZ Hydra
with Button module

## Slide 20: TinyCLR OS
Created by GHI Electronics
  https://www.ghielectronics.com/tinyclr/features
Can be ported to custom hardware
Modules hosted on NuGet
Not open source
  Though documentation is
Supports native C/C++ code
No Generics Support

## Slide 21: FEZ Board
Fast and Easy
Arduino Pin Compatible
$10 – Lowest Price
ARM Cortex-M4
512 KByte flash
96 KByte SRAM

## Slide 22: Other GHI Boards/Offerings
Universal Compute Modules
  Meant for Prototyping or low volume devices
  Switch out module while working
SurfaceMount Compute Modules
  Modules solder to board
  84MHz to 400 MHz chips
UCM
G120 SCM

## Slide 23: TinyCLR OS – Getting Setup
Follow simple instructions online
  https://docs.ghielectronics.com/software/tinyclr/getting-started.html
Install “TinyCLR OS Project System” Extension to VS
  https://marketplace.visualstudio.com/items?itemName=ghielectronics.tinyclr-projectsystem
Create new project

## Slide 24: TinyCLR Config
Application to update device Firmware
Debug board
Might need this on first use of new board

## Slide 25: Pros
No Generics Support
Can’t reference .NET Standard Libraries
Use Threads, not Tasks
Cons
NuGet Packages
Line-by-Line Debugging
Win10 IoT API