## Slide 1: .NET of Things

## Slide 2: This is:
Electronics
Native C/C++
Anything Internet related
This isn’t:
100 Level Overview
.NET

## Slide 3: Word Cloud
C#
.NET Core
.NET Standard
UWP
Micro Controller Unit (MCU)
Gadgeteer
.NET MicroFramework
TinyCLR OS
Meadow

## Slide 4: Misc Tools You’ll Need
SD Card Formatter
Disk Imager
  Win32 Disk Imager
Windows 10 IoT Core Dashboard
Plus your normal .NET Coding Tools

## Slide 5: Demo App
Based on outside light
  Turn spaceship lights on or off
Constantly polling light sensor
  Polling over I²C protocol

## Slide 6: I²C Protocol
Eye Squared See
Synchronous Protocol
Requires Hardware Support
Message Process
  Writing Data
    Write Out Register
    Write Out Each Byte
  Reading Data
    Write Out Register
    Read Each Byte

## Slide 7: SparkFun Ambient Light Sensor
APDS-9301
https://www.sparkfun.com/products/14350

## Slide 8: Raspberry Pi
“Low Resources”
  1.4 GHz 64 bit ARM CPU
  1 GB RAM
  Pi 3 B+
Exposed Pins
  The Money Maker

## Slide 9: Three Options with .NET
Windows 10 IoT
Mono on Raspberry Pi
.NET Core on Raspberry Pi

## Slide 10: .NET Standard 2.0+ Benefits

## Slide 11: Windows 10 IoT
Version of Windows for non-general purpose devices

## Slide 12: Good
Required OS updates every few years
Enterprise Programming Model
  Service vs. Client vs. Full App
  Headed vs. Headless
Hardware Specific
  Doesn’t run on MCUs
No quick start to creating a new App
  Copy/Paste existing examples
Ugly
Amazing tooling
Top Tier Debugging
  Line-by-Line
  Remote over network
Familiar to Windows Devs
  Remote PowerShell, Command Line

## Slide 13: Headed vs. Headless
Headed:
  Has a UI
  Single app starts on device startup
Headless:
  No UI
  UI Stack is disabled
    Black screen when monitor attached

## Slide 14: IoT Dashboard
Handles downloading Windows Versions
Puts Windows IoT onto SD Cards
Remotely connects to IoT Devices
  Run commands

## Slide 15: Windows 10 IoT - Getting Setup
Download/Install IoT Core Dashboard
  https://docs.microsoft.com/en-us/windows/iot-core/downloads
Create New Project in VS
  Blank App (Universal Windows)
  Manually make some changes
Debug Remotely
  VS can find the target device

## Slide 16: App Demo Time
UWP Background App

## Slide 17: .NET on Raspberry Pi
Running on Linux
Mono
.NET Core
  Pre/Post 3.0

## Slide 18: Good
Remote Debugging is Slow
Ugly
Can compile on board
Access to all Linux tools you’re used to
Mono tools not in .NET Core
  AOT Compiling
.NET Standard
Mono

## Slide 19: Good
Remote Debugging is Slow
Can’t compile .NET code on ARM chips
Ugly
Remote Debugging Exists
Access to all Linux tools you’re used to
.NET Core

## Slide 20: Pin Access
File API
  Linux loves File APIs
P/Invoke
  For performance
  Requires low-level code

## Slide 21: New in .NET Core 3.0
ARM 64 support for Linux
  Not Windows Yet
Pin Bindings for Raspberry Pi
  Open Source at github.com/dotnet/iot
Installed with Snap
  An app package manager
  sudo apt install snapd
  sudo snap install dotnet-sdk --beta --classic

## Slide 22: App Demo Time
Mono App
.NET Core 2.0 App
.NET Core 3.0 App

## Slide 23: .NET MicroFramework
Legacy
Designed for MCUs
  RAM ~300KB
  CPU like Cortex-M3 @ 120 MHz
Limited in features
  No generics
Limited MCU selection
Open Source
  http://netmf.github.io/
Netduino 2 courtesy of https://www.wildernesslabs.co/

## Slide 24: Cons
Limited Language Feature Support
  No Generics
Required VS Extension to begin
  Only worked on Community Version of VS
  Maxed out at VS 2015

## Slide 25: Gadgeteer
Extension of .NET MicroFramework
Easy Prototyping Platform
  Expensive
Open Source
  https://archive.codeplex.com/?p=gadgeteer
GHIElectronics FEZ Hydra
with Button module

## Slide 26: TinyCLR OS
Created by GHI Electronics
  https://www.ghielectronics.com/tinyclr/features
Can be ported to custom hardware
Modules hosted on NuGet
Not open source
  Though documentation is
Supports native C/C++ code
No Generics Support

## Slide 27: FEZ Board
Fast and Easy
Arduino Pin Compatible
$10 – Lowest Price
ARM Cortex-M4
512 KByte flash
96 KByte SRAM

## Slide 28: Other GHI Boards/Offerings
Universal Compute Modules
  Meant for Prototyping or low volume devices
  Switch out module while working
SurfaceMount Compute Modules
  Modules solder to board
  84MHz to 400 MHz chips
UCM
G120 SCM

## Slide 29: TinyCLR OS – Getting Setup
Follow simple instructions online
  https://docs.ghielectronics.com/software/tinyclr/getting-started.html
Install “TinyCLR OS Project System” Extension to VS
  https://marketplace.visualstudio.com/items?itemName=ghielectronics.tinyclr-projectsystem
Create new project

## Slide 30: TinyCLR Config
Application to update device Firmware
Debug board
Might need this on first use of new board

## Slide 31: Good
No Generics Support
Can’t reference .NET Standard Libraries
Use Threads, not Tasks
Closed Source
Ugly
NuGet Packages
Line-by-Line Debugging
Copies Win10 IoT API

## Slide 32: App Demo Time
TinyCLR OS App

## Slide 35: Meadow Board
Created by Wilderness Labs
.NET 2.0
  Runs on top of Mono Runtime
No Board -> No Demo
Documentation: beta-developer.wildernesslabs.co
Very Early Days

## Slide 37: Getting Setup
Purchase ST-Link V2
  For connecting Meadow board to host computer over USB
Follow OS Specific Instructions
  Windows: Install Vagrant and VirtualBox
  MacOS: Install Brew and Vagrant
Download ST-Link
Download dfu-uitil
  Device Firmware Upgrade Utilities
Flash Meadow Board with dfu-util