## Slide 1: .NET of Things
Online at: github.com/ProgrammerAl/Presentations-2019

## Slide 2: This is:
Electronics Deep Dive
Native C/C++*
Anything Internet related
This isn’t:
Compare and Contrast Overview
Interfacing with Hardware using .NET

## Slide 3: Demo App
Based on outside light
  Turn spaceship lights on or off
Constantly polling light sensor
  Polling over I²C protocol

## Slide 4: SparkFun Ambient Light Sensor
APDS-9301
https://www.sparkfun.com/products/14350

## Slide 5: I²C Protocol
Eye Squared See
Synchronous Protocol
Requires Hardware Support
Message Process
  Writing Data
    Write Out Register
    Write Out Each Byte
  Reading Data
    Write Out Register
    Read Each Byte

## Slide 6: Raspberry Pi
“Low Resources”
  1.4 GHz 64 bit ARM CPU
  1 GB RAM
  Pi 3 B+
Exposed Pins
  The Money Maker

## Slide 7: Three Options with .NET on Raspberry Pi
Windows 10 IoT
Mono over Linux
.NET Core over Linux

## Slide 8: .NET Standard 2.0+ Benefits

## Slide 9: Windows 10 IoT
Version of Windows for non-general purpose devices
Only supports certain chips/boards
Still Windows
  PowerShell, command line, .NET, etc

## Slide 10: Good
Required OS updates every few years
Enterprise Programming Model
  Service vs. Client
  Headed vs. Headless
No quick start templates built into VS
Ugly
Amazing tooling
Top Tier Debugging
  Line-by-Line
  Remote over network
Familiar to Windows Devs
  Remote PowerShell, Command Line
Free OS if no screen
  Or screen under 10”

## Slide 11: IoT Dashboard
Handles downloading Windows Versions
Puts Windows IoT onto SD Cards
Remotely connects to IoT Devices
  Run commands

## Slide 12: Windows 10 IoT - Getting Setup
Download/Install IoT Core Dashboard
  https://docs.microsoft.com/en-us/windows/iot-core/downloads
Create New Project in VS
  Install extension for new project templates
    https://marketplace.visualstudio.com/items?itemName=MicrosoftIoT.WindowsIoTCoreProjectTemplatesforVS15
Debug Remotely
  VS can find the target device

## Slide 13: .NET on Raspberry Pi
Running on Linux
Mono vs .NET Core (Pre/Post 3.0)

## Slide 14: Good
Doesn’t feel as loved as .NET Core
Ugly
Access to all Linux tools you’re used to
Mono tools not in .NET Core
  Compile on-board
  AOT Compiling
.NET Standard
On-board debugging
Installed with apt-get
Windows/MacOS/Linux Support
Mono

## Slide 15: Good
Remote Debugging is Slow
  Only on VS Code
Can’t compile on ARM chips
Ugly
Remote Debugging Exists
Access to all Linux tools you’re used to
GPIO Support for Raspberry Pi in .NET Core 3.0
Installed with apt-get, or downloading
  With Snap for 3.0
Windows/MacOS/Linux Support
.NET Core

## Slide 16: Pin Access
File API
  Linux loves File APIs
  Not available for all pins like I2C
P/Invoke
  For performance
  Requires low-level code

## Slide 17: Setting Up I2C Raspberry Pi Linux
Not on by default
Run `sudo raspi-config` to begin setup
https://learn.sparkfun.com/tutorials/raspberry-pi-spi-and-i2c-tutorial/all

## Slide 18: Compiling Apps
.NET Core
  Specify `linux-arm` architecture
  Self Contained if you desire
  Can’t be done on ARM device
  `dotnet publish ./RaspbianNetCoreDemo -c Release -r linux-arm --self-contained`
    ~\bin\Release\netcoreapp3.0\linux-arm\publish
  `dotnet RaspbianNetCoreDemo .dll`
Mono
  Can be done on ARM device
  Compile with MonoDevelop on Linux
  `mono RaspbianNetCoreDemo.exe`

## Slide 19: Code Review

## Slide 20: New in .NET Core 3.0
ARM 64 support for Linux
Pin Bindings for Raspberry Pi
  Open Source at github.com/dotnet/iot
Installed with Snap
  An app package manager
  sudo apt install snapd
  sudo snap install dotnet-sdk --beta --classic

## Slide 21: History Lesson - .NET MicroFramework
Legacy
Designed for MCUs
  RAM ~300KB
  CPU like Cortex-M3 @ 120 MHz
Open Source
  http://netmf.github.io/
Netduino 2 courtesy of https://www.wildernesslabs.co/

## Slide 22: Cons
Limited Language Feature Support
  No Generics
Limited MCU Selection
Required VS Extension to begin
  Only worked on Community Version of VS
  Maxed out at VS 2015

## Slide 23: TinyCLR OS
Created by GHI Electronics
  https://www.ghielectronics.com/tinyclr/features
Can be ported to custom hardware
Modules hosted on NuGet
Not open source
  Though documentation is
Supports native C/C++ code
No Generics Support

## Slide 24: FEZ Board
Fast and Easy
Arduino Pin Compatible
$10 – Lowest Price
ARM Cortex-M4
512 KByte flash
96 KByte SRAM

## Slide 25: TinyCLR OS – Getting Setup
Follow simple instructions online
  https://docs.ghielectronics.com/software/tinyclr/getting-started.html
Install “TinyCLR OS Project System” Extension to VS
  https://marketplace.visualstudio.com/items?itemName=ghielectronics.tinyclr-projectsystem
Create new project

## Slide 26: TinyCLR Config
Application to update device Firmware
Debug board
Might need this on first use of new board

## Slide 27: Good
No Generics Support
Can’t reference .NET Standard Libraries
Use Threads, not Tasks
Closed Source
Ugly
NuGet Packages
Line-by-Line Debugging
Copies Win10 IoT API

## Slide 28: Code Review

## Slide 29: Meadow Board
Created by Wilderness Labs
.NET Standard 2.0
  Runs on top of Mono Runtime
No Board -> No Demo
  Code is Available!
Documentation: beta-developer.wildernesslabs.co
Very Early Days

## Slide 32: Good
Very early days
  Beta product for now
Connecting over Vagrant VM is very different
Creating .NET Framework App/DLLs feels off
Ugly
NuGet Packages
Line-by-Line Debugging
Windows/MacOS/Linux Support

## Slide 33: Getting Setup - Dev Machine - Windows
Follow Instructions per OS
  Windows, Linux, and MacOS
Install VirtualBox
Install Vagrant
dfu-util*
  Used to send Meadow OS and/or Your App to Meadow board
  * This util comes with Vagrant setup. Download to your OS if you want to
Downloads Link
  http://beta-developer.wildernesslabs.co/guides/Getting_Started/Downloads/index.html

## Slide 34: Setup Vagrant
VM software for development machines
After installing, create a Working Folder
Download custom Vagrant file and config.sh from Wilderness Labs
Copy/Paste Vagrantfile and config.sh to Working Folder
From command line, run `vagrant up` to initialize the space

## Slide 35: Getting Board Setup
Purchase ST-Link V2
  For connecting Meadow board to host computer over USB
Download ST-Link software
Download dfu-util
  Device Firmware Upgrade Utilities
Flash Meadow Board with dfu-util

## Slide 36: Writing a Meadow App in VS
Create new Console App
  .NET Framework 4.7.1
  Same on MacOS, just extra steps
Add the Meadow.Core NuGet package
Change assembly name to app
  Meadow OS is hard coded to only run ‘app.exe’
  Not sure if this is temporary
Create any Class Libraries as .NET Framework
  Not Standard

## Slide 37: Deploying to/Running On a Meadow Board
Copy/Paste files from /bin to the ~/tmp folder in your Vagrant working folder
Start Vagrant VM
Connect ST-Link to Meadow
Within Vagrant, verify connection to Meadow with `lusb` command
Run `./start.sh &`
Start GDB with `gdb` command
At prompt, enter `target remote :4242`
Enter `c` to start your app.exe

## Slide 38: Code Review

## Slide 39: Extras
Hastlayer
  C# on FPGA
  Open Source
  https://hastlayer.com
Azure Functions for Edge Computing
  Deploy business-logic Azure Function code to device inside a Docker Container
  IoT Thing

## Slide 40: Shameless Self Promotion
@ProgrammerAL
programmerAL.com
Developer Side Quests Podcast